## Slide 1
CDC-Aware RTL Generation Benchmark
Can an LLM generate RTL that is both functionally correct and CDC/RDC-safe?
Latest result: GPT-5.6 Sol had 29 functional passes; JasperGold passed 0 of them.
Faiza · Advisor update · 24 August 2026
Faiza · CDC-aware RTL generation · 24 Aug 2026 1

## Slide 2
Motivation and research question
Faiza · CDC-aware RTL generation · 24 Aug 2026 2
Most RTL-generation work scores compilation and functional simulation.
Ordinary digital simulation does not model metastability or structural CDC/RDC safety.
A design may pass its testbench while retaining unsafe clock/reset crossings.
Research question: can generated RTL satisfy both function and CDC/RDC constraints?
Supported claim: functional pass does not imply CDC/RDC-clean.

## Slide 3
Benchmark and evaluation pipeline
Faiza · CDC-aware RTL generation · 24 Aug 2026 3
44 circuits packaged with RTL, TB, SDC, and Jasper.
Original and CDC/RDC-fixed RTL kept separate.
Golden RTL is never in the prompt; generated RTL is never edited.
Pilot: cdc_2phase, async_fifo, apbxclk.
Functional prompt: ports and behavior.
CDC-explicit: same, plus must be CDC/RDC-safe — no Gray/2-flop hints.
Frozen prompt
↓ Model-generated RTL
↓ Xcelium compile
↓ Functional simulation
↓ JasperGold CDC/RDC
↓ Pass@k + archived evidence

## Slide 4
Packaged CDC circuits: 44/44 tool-clean
Same layout as the pilot: original RTL, fixed RTL, testbench, SDC, Jasper
Faiza · CDC-aware RTL generation · 24 Aug 2026 4
Set | Count | Functional sim | JasperGold CDC/RDC
Frozen pilot | 11 | 11/11 PASS | 11/11 CLEAN
Catalog imports | 19 | 19/19 PASS | 19/19 CLEAN
Additional CDC circuits | 14 | 14/14 PASS | 14/14 CLEAN
Total packaged | 44 | 44/44 PASS | 44/44 CLEAN
Families added: Gray and 2-phase FIFOs, reset controllers, isochronous handshake, APB/AXI-Lite CDC, synchronizers.
These 44 are packaged references, not 44 LLM results. Specs for the extra 33 remain draft.

## Slide 5
Frozen one-shot baselines
Same scope: 3 circuits × 2 prompts × 3 attempts = 18 per model
Faiza · CDC-aware RTL generation · 24 Aug 2026 5
Model | Base | Compile | Functional | CDC-clean
Llama 3.3 70B Instruct | Llama | 4/18 | 0/18 | 0/18
RTLCoder-v1.1 4-bit GGUF | Mistral | 1/18 | 0/18 | 0/18
RTLCoder-DeepSeek-v1.1 fp16 | DeepSeek | 5/18 | 0/18 | 0/18
GGUF RTLCoder is Mistral-based. RTLCoder-DeepSeek is a separate fine-tune.
Typical failures: invalid assignments, truncation, broken APB, CDC timeout.
CDC-explicit wording alone did not produce a functional pass. Repair and Pass@20 are separate columns.

## Slide 6
Main result: GPT-5.6 Sol exposes the evaluation gap
3 circuits × 2 prompts × 10 attempts · compile → sim → Jasper after sim pass
Faiza · CDC-aware RTL generation · 24 Aug 2026 6
Circuit | Prompt | Compile | Functional | Jasper-clean
cdc_2phase | functional | 10/10 | 10/10 | 0/10
cdc_2phase | cdc_explicit | 10/10 | 10/10 | 0/10
async_fifo | functional | 10/10 | 0/10 | not run
async_fifo | cdc_explicit | 10/10 | 0/10 | not run
apbxclk | functional | 9/9 | 9/9 | 0/9
apbxclk | cdc_explicit | — | — | credits exhausted
29/29 sim passes failed Jasper. Typical tags: RST_PH_GLCH, RDC_RS_DFRS.

## Slide 7
Other protocols (not mixed into the Sol table)
One-shot, extra sampling, and repair stay in separate columns
Faiza · CDC-aware RTL generation · 24 Aug 2026 7
Protocol | Result | Takeaway
Llama compile-repair | 6/6 compile; 1/6 functional; 0 clean | Feedback fixes syntax, not CDC
RTLCoder-DeepSeek Pass@20 | 73 RTL; 7 compile; 0 functional | More samples found no sim pass
Jasper on those 7 compiles | 5 RDC fail; 2 zero crossings | Zero violations ≠ automatically clean

## Slide 8
Limitations
Faiza · CDC-aware RTL generation · 24 Aug 2026 8
LLM generation is still the 3-circuit pilot, not all 44 packaged circuits.
GPT-5.6 Sol is 49/60 complete; apbxclk CDC-explicit and one functional attempt remain.
OpenAI GPT-5.6 does not expose temperature, top-p, or seed.
RTLCoder-DeepSeek Pass@20 has no apbxclk yet.
Specs for the extra 33 circuits are still draft.
No synthesis, area, or assertion score yet.

## Slide 9
Proposed next phase
Faiza · CDC-aware RTL generation · 24 Aug 2026 9
Ask for this meeting
  Resume the remaining 11 GPT-5.6 Sol attempts after credits are added.
  Run one more API model on the same 3 × 2 × 10 loop.
After that
  Finish RTLCoder-DeepSeek Pass@20 when GPU is available.
  Expand generation from the 3-circuit pilot across the packaged 44.

## Slide 10
Thank you
Questions?
Compilation and simulation are necessary, but not sufficient, for generated CDC RTL.
Faiza · CDC-Aware RTL Generation · 24 August 2026
Faiza · CDC-aware RTL generation · 24 Aug 2026 10